## Slide 1: Report on review paper, computational methods for single-Particle electron cryomicroscopy
張子軒 黃峻祿
The paper’s doi: https://doi.org/10.1146/annurev-biodatasci-021020-093826 with supplemental appendix: https://www.annualreviews.org/doi/suppl/10.1146/annurev-biodatasci-021020-093826

## Slide 2: Content
Motivation and Introduction
  Overview of structural Biology
  X-Ray crystallography, nuclear magnetic resonance, and cryo-EM
  Example of a cryo-EM study
Image formation model
  The electron microscopy
  Phase-contrast imaging and the contrast transfer function (CTF)
  Direct electron detectors
Processing micrographs
  Motion correction
  Contrast Transfer Function Estimation and Correction
  Particle Picking
Three dimensional reconstruction
  Maximum Likelihood Estimation
  Expectation Maximization
  Bayesian Inference
  Maximum likelihood expectation maximization two-dimensional classification
  Stochastic gradient descent
Heterogeneity analysis
Evaluation of the maximum a posteriori probability and fitting the model
Future challenges

## Slide 3: Introduction
Main approach
in Cryo-EM
Multiple images take from same field , and tilt to different angles
SPR：single image takes from each field , randomly oriented and positioned particles
Given orientation
Grouped & Averaged
Pros & Cons in SPR
 | Pro | Con
 | X Crystallization → Simple & Save time | Large computation

## Slide 4: Overview of Structural Biology
The goal of structural Biology is to determine the macromolecules’ 3D structure in order to understand the way where machine* works.
The size of a macromolecule is described as its molecular mass or weight in daltons, Da.
  1 Da is about the mass of a hydrogen atom of 1 u, isotope mass.
  A large molecular machine might be a complex of multiple subunits totaling 1 MDa in molecular weight and have physical dimensions on the order of 200 angstroms ().
*Machines, such as a molecular motor or a solute transporter, pass through various conformations in the course of their reaction cycles. A complete understanding of their operation requires the multiple structures.
The atomic structure of a macromolecule is obtained by fitting an atomic model into a 3D density map.
  The resolution needs to be about 1.5 if individual atoms of carbon, nitrogen, etc., are to be located directly;
  A map of 3–4 resolution is sufficient to produce an informative atomic model.
3D density map
Molecular structure
Image from: Yin Chang-Cheng, Structural biology revolution led by technical breakthroughs in cryo-electron microscopy

## Slide 5: X-ray crystallography, nuclear magnetic resonance (NMR), cryo-EM
method | X-ray crystallography | NMR | Cryo-EM
source | X-ray | Magnetic dipole from spin of nucleus | electron
Forming image principle | Macromolecules are crystallized and are rotationally exposed to X-ray. A crystal produces diffracted beams which are recorded by detector. | Dipoles can jump onto a higher-energy state by exposure to a radio frequency field, then back to ground state. The measurement of this coupling that estimates the pairwise distance between atoms. Determine the global structure from the local distance estimates. | Macromolecules are interacted elastically with electron beam. The elastically scatterd electrons are recorded by detector.
Weakness | Radiation damage limits the X-ray dose and SNR. |  | Radiation damage limits the electron dose and SNR.
Difficulty | Purifying and crystallizing a sample of the macromolecule |  | 
X-ray crystallography, NMR and cryo-EM are methods to determine macromolecular structures. The below table shows the properties of each method.
To achieve the similar resolution, cryo-EM needs less macromolecules (104) than X-ray crystallography demand (108)

## Slide 6: The Electron microscope
The resolution of the electron microscope is related to the electron’s wavelength . The shorter wavelength can provide higher resolution.
  For example, when electrons are accelerated to energies for 100 to 300 keV. Theoretically, those electrons’ wavelengths range from about 0.037 to 0.02 .
  In practice, the resolution is limited to about 1 due to aberrations in the magnetic objective lens.
The structure of an electron microscope
100-300 keV

## Slide 7: Example of a cryo-EM study
A recent cryo-EM study [1] about determining the bacterial enzyme PaaZ is introduced in this review.
  PaaZ protein has two catalytic activities, a hydratase and a dehydrogenase, each having a distinct active site.
  With the solved structure, it was clear that the substrate pivots in a short tunnel connecting the active sites.
Cryo-EM specimens are consist of a film of 200-600 in thickness and are frozen at cryogenic temperature in a range of -150 to -273 °C.
The micrograph with particles which are selected in green circles. The error image of particle is selected in yellow circle. There’s an ice ball superimposed.
To compute the final 3D density map, 502 such micrographs, 118,000 particle images were extracted, of which 86,400 were used. Its 3D map will be shown later.
[1]: Sathyanarayanan N, et al. 2019. Molecular
basis for metabolite channeling in a ring opening enzyme of the phenylacetate degradation pathway.
Nat. Commun. 10:4127

## Slide 8: Phase-contrast imaging
Images are formed by exposing specimen to the electron beam, and cryo-EM detector records the transmitted electrons
  The electrons are scattered, either elastically or inelastically
  The majority of electrons recorded by the detector are those that pass through without any interaction, thus leading only to noise
α, scattering angle
z
α depends on the spatial frequency k of the electrostatic potential that the molecule creates.
z, the distance from the specimen to a image plane.

## Slide 9: Phase-Contrast Imaging and the Contrast Transfer Function (CTF)
The overall phase shift is
The total wave function includes the interference of the scattered wave with the unscattered wave
The probability of an electron being detected by the detector is proportional to which is written as:
, where is the frequency content of the sample.
The CTF H is the deviation from unity. . CTF tells how much contrast is transferred into the image.
For cryo-EM imaging, the important imaging mode is phase contrast.
  The elastically scattered electrons have shift their phase of the waves
  The phase shift depends on path length between the specimen and the plane
  The positive potential electron experiences results in a small phase advance. The average inner potential of water is about 5V, proteins, about 7.5 TeV

## Slide 10: The Contrast Transfer Function (CTF) and the Power Spectrum (PS)
The micrograph is given by :
  The point spread function, PSF, is the inverse Fourier transform of the CTF;
  is the electrostatic potential of the sample;
  is the tomographic projection operator and defined by . is the beam direction.
Take a Fourier transformation and a convolution becomes a product.
  Then we have where denotes the Fourier transform.
The power spectrum of the image is given by the squared magnitudes:
  The power spectrum vanishes on rings of radial frequencies that correspond to zero crossings of the CTF.
the experimental power spectrum
the circularly averaged PS
the fitted CTF2(|k|)
Blurred image
Notes: Ref. to look: https://www.zeiss.com/microscopy/int/solutions/reference/basic-microscopy/the-point-spread-function.html

## Slide 11: Direct electron detectors and beam-induced motion
Direct electron detector (DED) cameras were introduced into cryo-EM since 2012.
  DED cameras directly detect electrons even a single electron hit. This is highly efficient (better SNR) than CCD cameras.
  DED cameras have a high frame rate and can operate in a video mode, recording 40 frames during 2 s of exposure time.
There is movement of the specimen between individual movie frames. Particle movements are as large as 20 .
  This movement due to exposure is termed beam-induced motion, which may be related to inelastic scattering.
  Beam-induced motion causes the image blur which can be corrected by alignment of individual movie frames.
Apollo, direct electron detector camera, produced by Direct Electron Inc. Image from Direct Electron

## Slide 12: Progressing micrograph
First：Motion correction , CTF correction , particle picking
Second：2D classification, 3D reconstruction, and 3D heterogeneity analysis
Rely on classical image & signal processing
Statistical estimation & optimization

## Slide 13: Motion Correction
Motion Correction
Alignment
Average
 | Early method for motion correction
how | 
problem | particles move at different velocities and direction
solution | 
Relative motion
Least square
Frame shift
Velocity field
smooth with respect to
location,time
Be estimated
Dose-weighted averaging

## Slide 14: CTF estimation
Three defocus parameters of the CTF are estimated from the power spectrum of the whole micrograph:
  The power spectral density, PSD, of the micrograph ;
  The CTF H;
  The average PSD of the particles and other contaminants ;
  The PSD of the background noise .
The background term can be estimated by local averaging of the radial profile, by fitting a low-degree polynomial or by linear programming methods. The local minima of the background-subtracted PSD correspond to the zero crossings of the CTF, from which the defocus value can be estimated.

## Slide 15: CTF correction
Supposed we have image , object , and point spread function .

 . This is the CTF correction for giving better visual sense of object.
There are two difficulties that the zero crossings of the CTF and the decay of the envelope function at high frequencies.
  The CTF is zero at certain frequencies.
  The CTF amplitude is so low at high frequencies.
Another approach: Wiener filtering. Wiener filter minimizes the mean-squared error (MSE) among all linear filters and employs the spectral SNR (=).
Wiener filtering has better amplitude correction but information at zero cannot be recovered.
One approach: phase flipping. Convert the sign of H and apply to the images.
Image from here

## Slide 16: Particle picking
To meet 3D reconstruction input
Particle Detection
SNR
Contrast
Depend on
CTF (low frequency improve contrast)
By Volta Phase Plate
Cons : unstable , phase drift
Automatic picking
Heterogeneity analysis
 | Pros | Cons
Template matching | Simple Fast | Model bias (Einstein from noise)

## Slide 17: Three-dimensional reconstruction
3D reconstruction
Mathematical
Statistical
Computational
Difficulties of
reconstruction
Off-center
Distorted by CTF
Variability
Outlier
Compare with CT
 | Computerized Tomography | SPR
Pose Parameter | Known | Unknown
Noise | SPR > CT ( average out the noise ) | 

## Slide 18: Model of image for formation
We can model the electrostatic potential, , of the molecule which can be estimated from n noisy, CTF-affected projection images , in with unknow viewing angles. The model is written:
is the point spread function (PSF) of the -th image;
is the tomographic projection operator;
is an unknown 3 X 3 rotation matrix representing the unknown orientation of the -th particle;
denotes rotation of by .
The noise is represented by .
Models of image formation by defocus contrast
Protein PaaZ

## Slide 19: Maximum likelihood estimation
The 3D structure, , is the only parameter of interest from a structural biology standpoint. Other model parameters, such as image shifts,…etc., are considered nuisance parameters.

## Slide 20: Maximum likelihood estimation
The 3D structure, , is the only parameter of interest from a structural biology standpoint. Other model parameters, such as image shifts,…etc., are considered nuisance parameters.
Maximum likelihood estimation is adopted to find . We can define the maximum likelihood estimator (MLE) that maximizes the marginalized likelihood function, where marginalization is over all nuisance parameters, for instance . The likelihood function is written:
,
  is white Gaussian noise with pixel variance
  is the number of pixels in an image

## Slide 21: Maximum likelihood estimation
The 3D structure, , is the only parameter of interest from a structural biology standpoint. Other model parameters, such as image shifts,…etc., are considered nuisance parameters.
Maximum likelihood estimation is adopted to find . We can define the maximum likelihood estimator (MLE) that maximizes the marginalized likelihood function, where marginalization is over all nuisance parameters, for instance . The likelihood function is written:
,
  is white Gaussian noise with pixel variance
  is the number of pixels in an image
The marginalized likelihood function is obtained by integrating over the nuisance parameters. The function is:
.
  Then we insert then take log on , and we can obtain: ,
  The latter term can be used to determined the maximum MLE, .

## Slide 22: Expectation Maximization (EM)
ML-EM looks for ML or MAP estimates of parameters in models depending on latent variables .
  Guess the initial and then iterates between two steps, the expectation (E) step and the maximum (M) step, until convergence.
  An E step creates a function for the log-likelihood.
  A M step computes parameters maximizing the expected log-likelihood in the E step.

## Slide 23: Expectation Maximization (EM)
ML-EM looks for ML or MAP estimates of parameters in models depending on latent variables .
  Guess the initial and then iterates between two steps, the expectation (E) step and the maximum (M) step, until convergence.
  An E step creates a function for the log-likelihood.
  A M step computes parameters maximizing the expected log-likelihood in the E step.
In the E step of iteration t, with a given the current estimate of . For each , the parameter space is discretized with S fixed rotations . A vector of responsibilities (also known as weights or probabilities) of length S is computed as

## Slide 24: Expectation Maximization (EM)
ML-EM looks for ML or MAP estimates of parameters in models depending on latent variables .
  Guess the initial and then iterates between two steps, the expectation (E) step and the maximum (M) step, until convergence.
  An E step creates a function for the log-likelihood.
  A M step computes parameters maximizing the expected log-likelihood in the E step.
In the M step, a new estimate is defined as the maximizer of the log-likelihood of the images with the given responsibilities:
This is a linear least-square problem for which can be obtained by an existing methods for CT reconstruction.

## Slide 25: Expectation Maximization (EM)
ML-EM looks for ML or MAP estimates of parameters in models depending on latent variables .
  Guess the initial and then iterates between two steps, the expectation (E) step and the maximum (M) step, until convergence.
  An E step creates a function for the log-likelihood.
  A M step computes parameters maximizing the expected log-likelihood in the E step.
ML-EM increases the marginal likelihood in every iteration and converges to a critical point. However, one needs either a good initial or multiple-time running of ML-EM with different initializations.

## Slide 26: Computational complexity of ML-EM (1)
In the E step, it is to compute the . For images of size L x L:
  The latent variable space of SO(3) is discretized with rotations.
  is taken for different viewing directions on the unit sphere.
  Each of the sphere is in-plane rotated times.
The cost of projection-matching a single noisy image with a single projection image and all its in-plane rotations is .
  For n images, the cost of computing all responsibility vectors is .

## Slide 27: Computational complexity of ML-EM (1)
In the E step, it is to compute the . For images of size L x L:
  The latent variable space of SO(3) is discretized with rotations.
  is taken for different viewing directions on the unit sphere.
  Each of the sphere is in-plane rotated times.
The cost of projection-matching a single noisy image with a single projection image and all its in-plane rotations is .
  For n images, the cost of computing all responsibility vectors is .
In the M step, to compute tomographic projections of , the Fourier projection slice theorem is used.
  For sampling of size L x L, needs to be evaluated on off-grid points. Using NUFFT for efficiently computing in .
The M step involves a weighted tomographic reconstruction from the noisy images. The solution to the in the previous slide is:

## Slide 28: Computational complexity of ML-EM (2)
The cost of the E step is comparable to the cost of the M step, both given by. For instance, and L = 200 give nL4 = 1.6 x 1014.

## Slide 29: Accelerated ML-EM (1)
The common way to reduce the cost of the tomographic reconstruction step is by sparsification of the responsibility vector (by setting small weights to zero), whenever there is a high confidence in rotation assignment.
  In such cases, hard assignment of rotations (i.e., assigning the entire weight to the best-match rotation and zero weight to all other rotations) is much cheaper than soft assignment and still provides a similar output

## Slide 30: Accelerated ML-EM (1)
The common way to reduce the cost of the tomographic reconstruction step is by sparsification of the responsibility vector (by setting small weights to zero), whenever there is a high confidence in rotation assignment.
  In such cases, hard assignment of rotations (i.e., assigning the entire weight to the best-match rotation and zero weight to all other rotations) is much cheaper than soft assignment and still provides a similar output
Another way to reduce the cost of the M step is by using the gridding technique or a crude in interpolation instead of the more accurate NUFFT.
Computational savings for both the E and M steps are obtained by limiting the search space of the hidden variables.
  For example, the previous ML-EM iteration provides a good idea of the latent variable probabilities, and one can set a lower bound to limit the search space (bound method).

## Slide 31: Accelerated ML-EM (1)
The common way to reduce the cost of the tomographic reconstruction step is by sparsification of the responsibility vector (by setting small weights to zero), whenever there is a high confidence in rotation assignment.
  In such cases, hard assignment of rotations (i.e., assigning the entire weight to the best-match rotation and zero weight to all other rotations) is much cheaper than soft assignment and still provides a similar output
Another way to reduce the cost of the M step is by using the gridding technique or a crude in interpolation instead of the more accurate NUFFT.
Computational savings for both the E and M steps are obtained by limiting the search space of the hidden variables.
  For example, the previous ML-EM iteration provides a good idea of the latent variable probabilities, and one can set a lower bound to limit the search space (bound method).
The latent variable space can also be discretized at different levels of granularity.
  In adaptive EM, several grids are used for latent variable space of rotations and shifts. After a first swap over the coarse grid, only grid points that account for 99.9% (or some other fixed threshold) of the overall probability are kept, and then the search proceeds to the finer level that corresponds to these points.

## Slide 32: Accelerated ML-EM (2)
Subspace-EM accelerates ML-EM by reducing the dimensionality of the images using principal component analysis (PCA).
  Correlations between the projection images and the eigen-images (principal components) are precomputed.
  Then, correlations between projection images and the noisy experimental images are quickly evaluated as linear combinations of the precomputed correlations.
Our group contribution to image analysis by using PCA:
Szu-Chi Chung, et al., Two-stage dimension reduction for noisy high-dimensional images and application to Cryogenic Electron Microscopy, vol. 5 (2020), no. 2, 283-316. DOI
Ting-Li Chen, et al., An introduction to Multilinear Principle Component Analysis, JCSA, vol. 52 no. 1 (2013), 24-43. DOI

## Slide 33: Accelerated ML-EM (3)
Even with all these modifications, iterative refinement is often a computationally expensive step, especially if a high-resolution reconstruction or heterogeneity analysis is performed on large datasets.
It is also becoming more common for the reconstruction procedure to be applied to individual movie frames and to introduce more latent variables such as per-image defocus in order to reach higher resolution and squeeze as much as possible out of the data.
Specialized GPU (graphics processing unit) implementations have been recently developed to accelerate such large-scale computation.
  Our group contribution to the GPU-accelerated processing: Cryo-RALib -- a modular library for accelerating alignment in cryo-EM, by Szu-Chi Chung, et al. arXiv: 2011.05755

## Slide 34: Bayesian Inference
Large MSE
Poor coverage of slices in Fourier space
Small value of CTF at certain frequencies
Solution：Regularization
Prior on interest parameter
without
3D reconstruction may overfit
Basic idea behind Bayesian inference

## Slide 35: Bayesian Inference — Posterior
Prior distribution of
∵
Likelihood
Be estimated
maximum a posterior probability (MAP) estimate is obtained by
Posterior distribution
statistic of φ
Contribute to 3D reconstruction
Mean volume , confidence interval
Useful for model validation
Main concept in Bayesian inference — Posterior Distribution
Calculating the posterior distribution is out of reach
Variational inference to approximate posterior

## Slide 36: Bayesian Inference
Only information obtained about posterior distribution is mode.
MAP-EM
MAP estimate
MAP-EM
E step
M step :
a new structure is reconstructed that maximizes the posterior
given the conditional probabilities of the latent variables

## Slide 37: Bayesian Inference — Prior
Prior in SPR
The Fourier transform of
Unknown , model parameter
MAP 3D reconstruction update step includes a Tikhonov regularization parameter
Refine during EM iteration
Deal with ill-posed problem

## Slide 38: Bayesian Inference — Posterior
Masking
Masking
support of the molecule in real space is specified
values of φ outside the support are masked out and set to zero
Decreasing the parameter space and diminish noise increase resolution
Principle :
Mask iterative refinement
Practice :
First run
Of iterative refinement
Mask
Second run
Of iterative refinement

## Slide 39: ML-EM 2D classification
Image
Corresponding to
Similar viewing direction
Be aligned and averaged
2D class average
2D average
Input to ab initio structure estimation
Template for particle picking
provide assessment of particles and quality of the collected data
in-plane rotations
translations
class assignments
Latent Variable
EM
MLE of K class averages

## Slide 40: ML-EM 2D classification

## Slide 41: Stochastic Gradient Descent
MLE , MAP estimate require optimization second ordered method are not suitable
Classical gradient method : trapped in local optima
exact gradient : processing all image at once cost
Background of SGD
SGD decouple objective function into individual terms.

## Slide 42: Stochastic Gradient Descent
Gradient-based algorithms (Batch)
.
Step size (learning rate)
Inherent randomness of SGD help to escape local minima
Due to stochastic nature, SGD iterations never converge to global optimum
SGD is for low-resolution ab initio modeling

## Slide 43: Heterogeneity analysis
cryo-EM
Conformation
Can distinguish between a small number of distinct conformations, but the reconstruction of highly similar states and 3D movies of the continuum is hard
Characterize
structural variability
Composition
Covariance matrix approach
Normal mode of 3D analysis
Continuous heterogeneity (not require known rotations)
Manifold learning : for continuous variability

## Slide 44: Evaluation of MAP and fitting the model
Given the 3D reconstruction in the form of a density map, the final step is to fit an atomic model.
The PaaZ macromolecule
a) Overview of the PaaZ model, with
ribbons denoting the folding.
b) An end view of the model, obtained by a 90° rotation.
The validity of the model is dependent on the resolution of the map.
There are also techniques to test for errors in the creation of the map and in the estimation of its resolution

## Slide 45: Future challenge (1)
Protein denaturation
  A protein macromolecule is a linear polymer that folds into a particular shape. Most proteins unfold, which is denaturation, when they are exposed to hydrophobic environment. Exposed hydrophobic regions in neighboring proteins coalesce, yielding amorphous aggregates of misfolded proteins.
Specimen preparation
  A protein molecule diffuses rapidly and has many opportunities to diffuse up to the edge of the film. A layer of graphene oxide bounds the aqueous film. The fabrication of EM grids with graphene derivatives of good surface properties
  The preferred orientation of particles: many proteins orient with one surface interacting with the air-water interface or with a supporting film  resulting an uneven distribution of projection angles  leading to a poor 3D reconstruction.

## Slide 46: Future challenge (2)
The envelope function of the CTF, summarized by the B-factor, is the ultimate limitation of high resolution.
Unavoidable particle movement due to beam-induced rearrangement of water molecules in the vitreous ice.
  Water molecules move with a diffusion constant and produce Brownian motion of particles.
There is the possibility that rejected particles represent alternative conformations of the complex, or states in which there is more flexibility.
Quality control of data acquisition

## Slide 47: Backup

## Slide 48: Principle of 3D reconstruction of a macromolecule from EM images

## Slide 49: Motion correction
Motion correction refers to translational alignment and averaging of movie frames.
  The movement is not homogeneous across the field of view.
  The local motion can be estimated by cross correlating smaller image patches.
  If the velocity field is smooth w.r.t both location and time, the initial estimates can be fitted and interpolated by using local low-degree polynomials.
  After estimation of the velocity field, the frames are aligned and averaged.

## Slide 50: Mean squared error, MSE
The MSE of an estimator is the average squared difference between the estimated values and the actual value. So it is a measure of the quality of an estimator.

## Slide 51: Fourier projection slice theorem
This theorem is also called central slice theorem or projection slice theorem.
The theorem describes that images are projected along a given direction. The projected distribution is then taking the Fourier transformation. The result is corresponding to a line in the Fourier 2D space.

## Slide 52: Bayesian inference
where
  H stands for any hypothesis whose probability may be affected by data, E called evidence.
  , the prior probability, is the estimate of the probability of the hypothesis, H, before the data, E, is observed.
  E, the evidence, corresponds to new data that were not used in computing the prior probability.
  , the posterior probability, is the probability of H with the observed E, the probability of a hypothesis given the observed evidence.
  is the probability of observing E given H, and it is called likelihood.
  , this factor does not enter into determining the relative probabilities of different hypotheses because it is the same for all possible hypotheses being considered.

## Slide 53: Different function in time complexity