## Slide 1: ASCEP with Scipion3
鍾思齊
Courtesy of 蕭卉倫/林新閎

## Slide 2: Outline
Usage of Sever
Data source
ASCEP with Scipion3
  Workflow and IO
  Basic Usage

## Slide 3: ASCEP – Unified cryo-EM processing platform
Statistical tools build by our team
State-of-the-art packages
Dowload at: http://sabid.stat.sinica.edu.tw/
Notes: Additional packages:
Prime 3
EMAN2 for conversion
Xmipp3 for scipion
  RELION, CisTEM
  CryoSparc, SPHIRE(ISAC)

## Slide 4: Developing scipion3
Developer’s doc
  https://scipion-em.github.io/docs/docs/developer/tutorials/dev-tutorials
  https://scipion-em.github.io/docs/docs/developer/developers.html#extending-scipion
  https://scipion-em.github.io/docs/docs/developer/symmetries
Methods
  https://github.com/scipion-em
  https://github.com/phonchi/Computational-CryoEM

## Slide 5: Usage of Server

## Slide 6: Use our Server
Create account if you do not have one
Server IP: 140.109.74.85 (80 cores, 2GPU), 140.109.74.82 (88 Cores, 8 GPU)
Related programs
    FileZilla: https://filezilla-project.org/  Download/upload files
    Remote desktop
    MobaXterm: https://mobaxterm.mobatek.net/download.html  Command line, built-in X server
    Vnc-viewer : https://www.realvnc.com/en/connect/download/viewer/  Connect to specific session
    Putty +Xming : https://www.putty.org/ , https://sourceforge.net/projects/xming/
    Chimera: https://www.cgl.ucsf.edu/chimera/download.html

## Slide 7: FileZilla
檔案站台管理員連線
(第一次使用先按增新站台輸入資料確認)
.
在需要的下載或上傳檔案，
按下滑鼠右鍵會出現功能選項

## Slide 8: MobaXterm
第一次使用
先按session SSH 輸入IP  OK
在ssh 輸入echo xfce4-session > ~/.xsession

## Slide 9: Remote Desktop
這個工作列按滑鼠右鍵會出現，再點 Open Terminal Here，
就可以操作我們要用的指令
如果在terminal，無法開啟scipion，可以嘗試
輸入 source ~./bashrc

## Slide 10: Trouble shooting
在這個黑色框框，按右鍵會有選項
加入這兩項
此動作只是為了建造工作列，方便使用
下方Panel Preference 可調整工具列方向

## Slide 11: Trouble shooting
Enable the Tab
Change it to empty
After modification, You may need to kill the old session to enable it

## Slide 12: Useful commands
htop  查看CPU 使用量
nvidia-smi 查看GPU 使用量
https://www.guru99.com/linux-commands-cheat-sheet.html

## Slide 13: Data Source

## Slide 14: Data Source
Tutorial data:
  /nas2/CryoEM_data
EMPIAR
  /nas2/
ASCEM
  /nas2/cryoEM_data
Additional
  /nfs/

## Slide 15
Dataset | Data | Model | Size | Res. | (Height, width) Pixel Size | Movie #(frame) | Particles | 
Beta-Gal | EMPIAR-10017 | EMD-2824 | 5.3GB | 4.2A (D2) | (4096,4096) 1.77 | 84(1) MRC | ? | Scheres
Relion2 | Tutorial |  | 4 GB | 7.3A (D2) | (1950,1950) 3.54 | 15(1-16) MRC | ? (100) | Scheres
Denosing get 7.3A |  |  |  |  |  |  |  | 
70S Ribosome | Test_Data | EMD-1056 | 0.7GB | 9A (C1) | ? 2.82 | ? | 10000 (130) | Scheres
80S Ribosome | EMPIAR-10028 | EMD-2660 | 1.2TB | 3.2A (C1) | (4096,4096) 1.34 | 1081 (1-16) TIFF | 105247 (360) | Scheres
Beta-Gal | EMPIAR-10204 | EMD-6840 | 321.4GB | 2.6A (D2) | (3710,3838) 0.885 | 1338 (1-49) TIFF | ? | Kato
Relion3 | Tutorial |  | 3.1GB | 2.9A (D2) | (3710,3838) 0.885 | 24 (1-24) TIFF | ? (256) | Scheres
Denosing get 3.17A |  |  |  |  |  |  |  | 
tri-snRNP | EMPIAR-10073 | EMD-8012 | 75.2GB | 3.7A (C1) | ? 1.43 | ? | 473827 (3380) | Scheres
Dataset | Data | Model | Size | Res. | (Height, width) Pixel Size | Movie #(frame) | Particles | 
Beta-Gal | EMPIAR-10017 | EMD-2824 | 5.3GB | 4.2A (D2) | (4096,4096) 1.77 | 84(1) MRC | ? | Scheres
Relion2 | Tutorial |  | 4 GB | 7.3A (D2) | (1950,1950) 3.54 | 15(1-16) MRC |  | Scheres
Denosing get 7.3A |  |  |  |  |  |  |  | 
70S Ribosome | Test_Data | EMD-1056 | 0.7GB | 9A (C1) | ? 2.82 | ? |  | Scheres
80S Ribosome | EMPIAR-10028 | EMD-2660 | 1.2TB | 3.2A (C1) | (4096,4096) 1.34 | 1081 (1-16) TIFF |  | Scheres
Beta-Gal | EMPIAR-10204 | EMD-6840 | 321.4GB | 2.6A (D2) | (3710,3838) 0.885 | 1338 (1-49) TIFF | ? | Kato
Relion3 | Tutorial |  | 3.1GB | 2.9A (D2) | (3710,3838) 0.885 | 24 (1-24) TIFF |  | Scheres
Denosing get 3.17A |  |  |  |  |  |  |  | 
tri-snRNP | EMPIAR-10073 | EMD-8012 | 75.2GB | 3.7A (C1) | ? 1.43 | ? |  | Scheres

## Slide 16
Dataset | Method | Date | Size |  | Res. | Pixel Size |  | Movie |  | Particles | 
GS data | Krios+Falcon III |  | 60GB |  | ? | ? 0.85 |  | 558 MRC |  | 94154 (400400) | KpWu
Heterogenity observed using DRMRA |  |  |  |  |  |  |  |  |  |  | 
GS-Y398F-APO form |  | 2018.08.23 | 938 GB | ? (O) |  |  | (4096,4096) 0.85 |  | 603 (1-50) MRC | ? | KpWu
Apo-ferritin in RELION-3.0 | EMPIAR-10200 | EMD-0144 | 191.5 GB | 1.65A (O) |  |  | (3838,3710) 0.814 |  | 1255(1-40) TIFF | ? | Scheres
Apoferritin | Krios+Falcon III | 2018.08.30 | 643 GB | 2.7A (O) |  |  | (4096,4096) 0.85 |  | 411 (1-50) MRC | 86856 () | KpWu
Denoising from scratch get 6A |  |  |  | 3.48/3.04A (O) |  |  |  |  | 10 (1-50) | 4096 () | Apo_10
Apoferritin | Krios | 2018.11.08 | 469GB | 2.18 (O) |  |  | (4096,4096) 0.85 |  | 1022->300 (1-50) MRC | 368774 () | KpWu
 |  |  |  |  |  |  |  |  |  |  | Apo_11
Apoferritin | Krios | 2018.11.10 | 8TB | 1.96 (O) |  |  | ? 0.53 |  | 2600 (1-100) MRC |  | KpWu
Dataset | Method | Date | Size |  | Res. | Pixel Size |  | Movie |  | Particles | 
GS data | Krios+Falcon III |  | 60GB |  | ? | ? 0.85 |  | 558 MRC |  |  | KpWu
Heterogenity observed using DRMRA |  |  |  |  |  |  |  |  |  |  | 
GS-Y398F-APO form |  | 2018.08.23 | 938 GB | ? (O) |  |  | (4096,4096) 0.85 |  | 603 (1-50) MRC | ? | KpWu
Apo-ferritin in RELION-3.0 | EMPIAR-10200 | EMD-0144 | 191.5 GB | 1.65A (O) |  |  | (3838,3710) 0.814 |  | 1255(1-40) TIFF | ? | Scheres
Apoferritin | Krios+Falcon III | 2018.08.30 | 643 GB | 2.7A (O) |  |  | (4096,4096) 0.85 |  | 411 (1-50) MRC |  | KpWu
Denoising from scratch get 6A |  |  |  | 3.48/3.04A (O) |  |  |  |  | 10 (1-50) |  | Apo_10
Apoferritin | Krios | 2018.11.08 | 469GB | 2.18 (O) |  |  | (4096,4096) 0.85 |  | 1022->300 (1-50) MRC |  | KpWu
 |  |  |  |  |  |  |  |  |  |  | Apo_11
Apoferritin | Krios | 2018.11.10 | 8TB | 1.96 (O) |  |  | ? 0.53 |  | 2600 (1-100) MRC |  | KpWu

## Slide 17
Dataset | Data | Model | Size | Res. | Pixel Size | Movie | Particles | 
Brome Mosaic virus | EMPIAR-10010 | EMD-6000 | 1.7TB | 3.8A (I) | (4096,3072) 0.99 | 424 (1-37) TIFF | 35142 (420) | Wah Chiu
T20S | EMPIAR-10025 | EMD-6287 | 2.0TB | 2.8A (D7) | (7420,7676) 0.6575 | 196 (1-38) MRC | 49955 (448) | Carragher
CryoSparc | Tutorial |  | 8.1GB | 2.93A (D7) | (7420,7676) 0.6575 | 20 (1-38) TIFF | (4400) | CryoSparc
TRPV1 | EMPIAR-10059 | EMD-8117 | 93.8 GB | 2.95A (C4) | (3838,3710) 1.2156 | 1200(1) MRC | 218805 (192,192) | Gao and Cheng
Apo-Ferritin | EMPIAR-10248 |  | 145.9 GB | 1.54A (O) | (3710,3838) 0.495 | 972 (1-50) TIFF | ? | Kato
CisTEM | EMPIAR-10146 |  | 5.6GB | 3A (O) | (1240, 1200) 1.5 | 20 (1-50) MRC | ? | CisTEM
alcohol dehydrogenase | EMPIAR-10249 | EMD-0406 | 1.3T | 2.9A (C2) | (3710,3838) 0.5585 | 1153 (1-44) MRC | ? | Lander
Met-hemoglobin | EMPIAR-10250 | EMD-0407 | 1.9T | 2.8~3.2A (C2) | (3710, 3838) 0.5585 | 1665 (1-44) MRC | ? | Lander
PKA | EMPIAR-10252 | EMD-0409 | 5.5T | 6A (C1) | (3710, 3838) 0.5585 | 4812 (1-44) MRC | ? | Lander
Dataset | Data | Model | Size | Res. | Pixel Size | Movie | Particles | 
Brome Mosaic virus | EMPIAR-10010 | EMD-6000 | 1.7TB | 3.8A (I) | (4096,3072) 0.99 | 424 (1-37) TIFF |  | Wah Chiu
T20S | EMPIAR-10025 | EMD-6287 | 2.0TB | 2.8A (D7) | (7420,7676) 0.6575 | 196 (1-38) MRC |  | Carragher
CryoSparc | Tutorial |  | 8.1GB | 2.93A (D7) | (7420,7676) 0.6575 | 20 (1-38) TIFF |  | CryoSparc
TRPV1 | EMPIAR-10059 | EMD-8117 | 93.8 GB | 2.95A (C4) | (3838,3710) 1.2156 | 1200(1) MRC | 218805 (192,192) | Gao and Cheng
Apo-Ferritin | EMPIAR-10248 |  | 145.9 GB | 1.54A (O) | (3710,3838) 0.495 | 972 (1-50) TIFF | ? | Kato
CisTEM | EMPIAR-10146 |  | 5.6GB | 3A (O) | (1240, 1200) 1.5 | 20 (1-50) MRC | ? | CisTEM
alcohol dehydrogenase | EMPIAR-10249 | EMD-0406 | 1.3T | 2.9A (C2) | (3710,3838) 0.5585 | 1153 (1-44) MRC | ? | Lander
Met-hemoglobin | EMPIAR-10250 | EMD-0407 | 1.9T | 2.8~3.2A (C2) | (3710, 3838) 0.5585 | 1665 (1-44) MRC | ? | Lander
PKA | EMPIAR-10252 | EMD-0409 | 5.5T | 6A (C1) | (3710, 3838) 0.5585 | 4812 (1-44) MRC | ? | Lander

## Slide 18: ASCEP with Scipion3

## Slide 19: Install ASCEP
Install scipion3 http://scipion.i2pc.es/
Install scipion-em-relion, scipion-em-eman2, scipion-em-xmipp, scipion-em-cryosparc2, scipion-em-chimera
scipion3 conf
gedit scipion/config.py
  ASCEP_DIR=/path/to/ascep
  EMAN231DIR=/path/to/ascep
Modify the cuda path in scipion-em-ascep/ascep/__init__.py (cupy-cudaxx)
scipion3 install –p /path/to/scipion-em-ascep/--devel

## Slide 20: Enable Scipion3
gedit ~/.bashrc
  Add export PATH=/home/iping/scipion3/:$PATH to the end the file
source ~/.bashrc
scipion3 config
  Press any key other than Enter

## Slide 21: Import Project
直接在指令視窗打 scipion3 即可開啟~~

## Slide 22: Import/Export workflow
按下Create，就會出現操作介面->import workflow /home/iping/workflow_ascep.json

## Slide 23: Upload workflow
http://workflows.scipion.i2pc.es/

## Slide 24: Upload workflow

## Slide 25: Import/Export metadata/binaries
Use ctrl+a to select all blocks and right click to export workflow
Use crtl+f to search protocol

## Slide 26: Basic Usage

## Slide 27
指令區
執行區
說明區
查看結果

## Slide 28
如果進到操作介面是凌亂的情況，或者需要對流程做整理，點選此圖，程式會自行整理順序。
可切換模式

## Slide 29
框框的顏色分為四種
1.藍色:代表只儲存操作指令，並未執行。
2.綠色:指令執行完。
3.黃色:指令執行中。
4.淡黃色:指令執行結束，還可以點進去繼續執行，
但底下有接其他指令不可再執行會出現錯誤。
5.紅色:出現錯誤。

## Slide 30
點選框框，按下滑鼠右鍵，會出現一排的選項，
:會出現指令操作
:複製此次的指令操作
:刪除此次操作，但有連接下一步，則無法刪除
:此次操作所存的檔案位置
:停止此操作，只有在運行中的指令才會出現
其他比較少使用就不介紹，但是可以去玩玩看。

## Slide 31
點選其中一個框框，在說明區會出現該指令的說明
1.Summary:
該指令輸入及輸入的資料訊息。
2.Method :方法說明及references。
3.Output Log: 程式執行過程。
以此圖為例，我們可以看到這個指令的
輸入資料是 outputMicrographs ，有14筆資料，pixel size為 2.82 A。
輸出資料是 outputParticles，有10000筆資料，影像大小130130， pixel size為2.82 A。

## Slide 32
錯誤情況判斷查閱說明區 Output Log run stdout
若沒有出現紅字，有可能是執行到一半斷掉，重新執行即可。
若出現紅字，先改放入參數，再重新執行，或者選擇其他指令執行!!!

## Slide 33: Imports
點選
依照資料選擇輸入方式
1.資料檔案位置
2.資料名稱
*.mrc 代表讀取所有的 .mrc檔
填寫
Save 只會儲存輸入的訊息，並不會執行，
Execute 會儲存及執行此步驟。
3.按下Execute ，
執行此過程。
1
2
3

## Slide 34: 查看執行結果
由這裡可知共有15個movie，a每個movie有16張影像，
影像大小1950
1
2
點選這個綠色框框
點Aanlyze Results
點兩下會出現單張影像的圖像。
3

## Slide 35: Particle picking
1
2
按 找到要輸入的資料
3
4
圈選工具
圈particle 的標示
連續圈選，不好用
橡皮擦，用來刪除框框
調整框框size，可以先圈一個particle，再來回調整
下一頁
5
圈 particle
6
圈了一些particle 在按這個按鈕

## Slide 36
第6步這個動作會讓程式自己圈選，但是可以看到黃色框框區域還有些沒選到
7
按下 Reset Micrographs 使之全部重選
調整Threshod會影響最後particle選入的數量
8
9
在此只需做完一張 mircographs的 particle picking，其他張使用
Auto-picking

## Slide 37: Extract
1
2
3
按 找到要輸入的資料，
Particle box size 自行調整
Invert contrast : Yes !!
4
1. Invert contrast 改變 particle 的顏色，
慣用 白色 particle。
白色
黑色
2. Recommend
Xmipp extraction- for xmipp, eman2, sparx
Reion extraction- for cryosparc2 and relion (Especially in 3D part)
3. Bin the particle to speed up processing before 3D Refinement

## Slide 38: https://scipion-em.github.io/docs/docs/user/scipion-gui.html
隨意一張圖按下滑鼠右鍵會出現選項
Enable: 選入這個class
Disable:不要這個class
像這種只要丟棄第一個class，可以先對第一個class 點選disable，在點
SelectALL。
2
1
ShowJ (Connect with ImageJ and Chimera)

## Slide 39
1
點選這個綠色框框
點Aanlyze Results
2
可以看到particle 的分層，如果想看3D圖，
點選chimera
ShowJ

## Slide 40
當你點下Aanlyze Results，並沒有出現分組結果，而是出現下列這些框框，此時請點 ，
就會出現執行結果。
relion
cl2d
Other viewer/statistics

## Slide 41: MPI/GPU
1
2
按 找到要輸入的資料
3
使用CPU個數，可自行調整，

## Slide 42: MPI/GPU
浮標指向其中一個框框，停留一段時間，會出現該指令執行時間。

## Slide 43: Break
Manual
https://github.com/I2PC/scipion/wiki/tutorials/scipion_tutorial_betagal.pdf
Or 卉倫的ppt

## Slide 44: ASCEP

## Slide 45: ASCEP: More Competitive Algorithms to Meet Current Challenges
2SDR
i-tSNE
DRMRA
Robust PCA
CNN
CryoSparc
ISAC
PRIME
Model Bias
Still growing…
DRMRA
Network

## Slide 46: ASCEP : Enable us to select a best workflow – pMMO molecule
(Wei-Hau Chang , Hsin-Hung Lin , I-Kuen Tsai, Shih-Hsin Huang , Szu-Chi Chung , I-Ping Tu , Steve Yu, Sunney I. Chan, “Copper Centers in the Cryo-EM Structure of Particulate Methane Monooxygenase Reveal the Catalytic Machinery of Methane Oxidation”, Accepted by Journal of the American Chemical Society. , (2021).)
Notes: electrostatic potential

## Slide 47: ASCEP – CryoRALib
Multiple initial 2D models will be generated through clustering of the raw dataset
  This procedure works well under low SNR settings
Particle images
Orientation parameters
…
Max
Calculate CC in
different
PCA+Kmeans
50~500
2D models
(Szu-Chi Chung, Cheng-Yu Hung, Huei-Lun Siao, Hung-Yi Wu, Wei-Hau Chang, I-Ping Tu, “Cryo-RALib –
a modular library for accelerating alignment in cryo-EM ”, Accepted by IEEE International Conference on Image Processing (ICIP) , (2021).)
Notes: The goal is to obtain the 3D structure, that is the roughly 10^6 voxel values in a 3D density map, from perhaps 10^9 very noisy pixels in a dataset
of particle images. To solve the structure, ideally one would examine all possible density maps and pick the single one
that best matches the dataset, given a scoring function such as the squared error or the likelihood.
one comfort is that the gross misassignment of angles generally results in low-resolution reconstructions. Thus, it is to be hoped that an interpretable,
high-resolution map is unlikely to suffer from model bias.
When the data quality is high, convergence to the global optimum is quite reliable and initial models such as smooth ellipsoids or random densities result in correct structures.
However, when the SNR of the images is low or when preferential particle orientation causes the strong overrepresentation of certain projection directions, model bias can be severe
Reliable 3D model using stochastic approach or experiment (tilt-pair analysis, random conical tilt)
Find the set of parameters that most likely determine the observed data
Discrete parameter assignment are replaced by probability-weighted integrations over all possible assignments
Each image is assigned by all orientations and classes with weights
0≤φ≤360, 0≤θ≤180, 0≤ψ≤360

## Slide 48: 2SDR method
Solving eigenvectors of covariance matrix with size is
(size: )
(size: )
Assuming
(size: )
(size: )
(size: )
(size: )
PCA
(“Two-stage dimension reduction for noisy high-dimensional images and application to Cryogenic Electron Microscopy”, Annals of Mathematical Sciences and Applications, 2020)

## Slide 49: ASCEP – 2SDR
SetOfParticles
deselect to use PCA
deselect to use MPCA

## Slide 50
Can be used with downstream analysis

## Slide 51: 2SDR denoising helps on alignment – PrePro
Orientation
parameters
Reference-Based
Alignment
Orientation
parameters
2SDR
CCC
CCC
Transform

## Slide 52: 2SDR denoising helps on alignment – PrePro [6]
Using 70S ribosome
  21 most correlated images are averaged using original data
With 2SDR
Without 2SDR
Reference
Orientation
parameters
Reference-Based
Alignment
Orientation
parameters
2SDR
CCC
CCC
Transform
Ground Truth
(“Pre-Pro is a Fast Pre-Processor for Single-Particle Cryo-EM by Enhancing 2D Classification”, Communications Biology, 2020)
Notes: It will be helpful in alignment

## Slide 53: ASCEP – PrePro
Seldom used
Expected radius in pixel
Specify MPI and GPU

## Slide 54
For DRMRA
Already aligned!
Average

## Slide 55: rAMI –Rapid Alignment with Moment of Inertia for Cryo-EM Image Processing
Denoise by 2SDR
Compute and solve eigenvectors
Align major axis with -axis
Fine-tune by checking the flip and rotation
Denoised image
MoI
MoI_rf
rAMI
RFA
Noisy image
(Szu-Chi Chung, Shao-Hsuan Wang, Cheng-Yu Hung, Wei-Hau Chang, I-Ping Tu, “rAMI –Rapid Alignment with Moment of Inertia for Cryo-EM Image Processing”, Accepted by Microscopy and Microanalysis 2021 Meeting , (2021).)

## Slide 56: rAMI –Rapid Alignment with Moment of Inertia for Cryo-EM Image Processing
Betagal
70S ribosome

## Slide 57: ASCEP – RAMI
Feed into RFA

## Slide 59: -SUP (Self-Updating Process)
Different influence region (attraction force)
  Do not need to specify the number of cluster or the random initialization of centers
  Robust to outlier (contaminates)
(Chen, Ting-Li and Hsieh, Dai-Ni and Hung, Hung and Tu, I-Ping and Wu, Pei-Shien and Wu, Yi-Ming and Chang, Wei-Hau and Huang, Su-Yun. -SUP: A clustering algorithm for cryo-electron microscopy images of asymmetric particles.” The Annals of Applied Statistics, 8(1), 259-285. (2014))
Notes: 27 points

## Slide 60: ASCEP – R-SUP
From dimensional reduction method
Can use r-estimator
The size of outlier class
Larger value means we collect larger neighborhood into the same cluster

## Slide 61
Other value of tau, dyna,ically computed
Select according to maximum of
Outlier will be put into max class number

## Slide 62: ASCEP - Clustering
Different algorithm will have different parameters

## Slide 63: DRMRA

## Slide 64: DRMRA (a--SUP )
Data matrix , samples with features, tuning parameter ()
  Iter
  Start with
  Repeat
  tree = construct_Tree_or_hash({})
    For
    NN = tree.nearestNeighbor()
    End
    Iter = Iter+1
  Until convergence
  Output cluster centers and cluster membership
Space-partition tree is used
  Reduce pairwise-distance calculation to or
Dynamic SUP is employed
  Increase in each iteration
  Focus on local structure at the beginning
Finding working parameter
  A coarse-grained binary search to find the range of nontrivial solution
  Grid search on the range
Notes: https://github.com/google-research/google-research/tree/master/scann?fbclid=IwAR0CcYkdtLpzjrjA6RZT7XqT5HdKxicrRwNNL8-Xx-gQxW3KdFmwmOUAaHU
construct_Tree_or_hash
  Exact (O(𝑝𝑛 log⁡〖𝑛)〗)
    Vantage-point tree (BH2014)
    Ball-tree (sklearn)
  Approximate (O(𝑝𝑛))
    Nearest Neighbor Descent (Flt-tsne, Open-tsne)
    Faiss (cuml, tsne-cuda)
t-SNE 𝑘 set to 3𝑢~150
We may also consider the cell interaction instead of point interaction

## Slide 65
Only use a few classes for alignment
Correct CTF, put full size image here
From PrePro
Partition the dataset, usually 5000~20000
Use t-SNE to generate initial class averages
Adjust C in the final
round

## Slide 66
Cleanup for downstream analysis

## Slide 67: ASCEP – GPU ISAC/CryoRALib
EQ-Kmeans

## Slide 68: t-SNE (Manifold Learning)
Input in dimension
Output in 2 or 3 dimension
PCA/2SDR embedding
t-SNE
(Maaten, Laurens van der, and Geoffrey Hinton. "Visualizing data using t-SNE." Journal of machine learning research 9.Nov (2008): 2579-2605.)
Notes: http://www.datakit.cn/blog/2017/02/05/t_sne_full.html

## Slide 69: ASCEP – ITSNE, TSNE, TRANSFORM
Select yes for particles for DRMRA or ISAC
For other classification tasks

## Slide 70
1) Use Lasso tool or Box select
2) Save the selection class
3) Press close if you are done

## Slide 71: Other methods
2D conformation analysis based on network
CNN for auto selection of classes
3D methods
Other Issue
  CTF and phase plate

## Slide 72: Advance

## Slide 73: 尋找輸出資料路徑
點選需要的輸出資料的框框，按下滑鼠右鍵，會出現一排的選項，點取 Brower
大多數的資料都存在extra 裡面
1
2
3
有了路徑就能從外部的資料夾找到檔案，
也可以透過 ftp直接到從資料夾載資料。

## Slide 74: 下載需要的參數資訊
點選需要的輸出資料的框框，按下滑鼠右鍵，會出現一排的選項，點取 Brower
1
2
3
點選有 這個符號的檔案
下一頁
4
點選Browse Data
假設今天我想下載 movement alignment 的位移資訊

## Slide 75
找到我們要的資料位置，
在此為c13、c14
5
6
將Table的地方調成Objects
複製c13、c14行的資料到這裡
7
8
10
調整檔案位置及名稱，名稱記得打上 .txt
9

## Slide 76: Recommend method
Stage | CPU | GPU
Motion Correction | Unblur | MotionCor2
CTF Estimation | Ctffind4 | Gctf
Particle Picking | Xmipp Relion | CrYolo Topaz
Alignment | RAMI PrePro | PrePro
2D Classification | ISAC CL2D DRMRA | GPU ISAC Relion CryoSparc DRMRA
2D Validation | i-tSNE t-SNE 2SDR | 

## Slide 77
3D Initial Model | Simple Eman2 | CryoSparc
3D Classification/ Validation | Xmipp Validation tool | Relion 3D Classification/Multibody Refinement CryoSparc Nonuniform/Local Refinement
3D conformation analysis |  | 3DVA CryoDrgn
3D Refinement | Xmipp High Res | Relion CryoSparc
Polishing |  | Relion CTF Refinement Relion Bayesian Polishing