## Slide 1: ASCEP with Scipion2
鍾思齊
Courtesy of 蕭卉倫/I2PC

## Slide 2: Outline
Usage of Sever
Data source
ASCEP with Scipion2
  Workflow and IO
  Basic Usage
  Consensus and Validation protocols
Model building

## Slide 3: Usage of Server

## Slide 4: Use our Server
Create account if you do not have one
Server IP: 140.109.74.100 (88 cores, 8GPU), 140.109.72.119 (80 Cores, 1 GPU)
Related programs
    FileZilla: https://filezilla-project.org/  Download/upload files
    Remote desktop
    MobaXterm: https://mobaxterm.mobatek.net/download.html  Command line, built-in X server
    Vnc-viewer : https://www.realvnc.com/en/connect/download/viewer/  Connect to specific session
    Putty +Xming : https://www.putty.org/ , https://sourceforge.net/projects/xming/
    Chimera: https://www.cgl.ucsf.edu/chimera/download.html

## Slide 5: FileZilla
兩種方式
1.檔案站台管理員連線
(第一次使用先按增新站台輸入資料確認)
2.
在需要的下載或上傳檔案，
按下滑鼠右鍵會出現功能選項

## Slide 6: MobaXterm
第一次使用
先按session SSH 輸入IP  OK
接下來只要點選這個就可以進到server

## Slide 7: Remote Desktop
這個工作列按滑鼠右鍵會出現，再點 Open Terminal Here，
就可以操作我們要用的指令
如果在terminal，無法開啟scipion，可以嘗試
輸入 source ~./bashrc
source /etc/environment

## Slide 8: Trouble shooting
在這個黑色框框，按右鍵會有選項
加入這兩項
此動作只是為了建造工作列，方便使用
下方Panel Preference 可調整工具列方向

## Slide 9: Trouble shooting
Enable the Tab
Change it to empty
After modification, You may need to kill the old session to enable it

## Slide 10: Useful commands
htop  查看CPU 使用量
nvidia-smi 查看GPU 使用量
export CUDA_VISIBLE_DEVICES=2,3
 鎖定 GPU

## Slide 11: Data Source

## Slide 12: Data Source
Tutorial data:
  /nas2/CryoEM_data
EMPIAR
  /nas2/
ASCEM
  /nas2/cryoEM_data

## Slide 13
Dataset | Data | Model | Size | Res. | (Height, width) Pixel Size | Movie #(frame) | Particles | 
Beta-Gal | EMPIAR-10017 | EMD-2824 | 5.3GB | 4.2A (D2) | (4096,4096) 1.77 | 84(1) MRC | ? | Scheres
Relion2 | Tutorial |  | 4 GB | 7.3A (D2) | (1950,1950) 3.54 | 15(1-16) MRC | ? (100) | Scheres
Denosing get 7.3A |  |  |  |  |  |  |  | 
70S Ribosome | Test_Data | EMD-1056 | 0.7GB | 9A (C1) | ? 2.82 | ? | 10000 (130) | Scheres
80S Ribosome | EMPIAR-10028 | EMD-2660 | 1.2TB | 3.2A (C1) | (4096,4096) 1.34 | 1081 (1-16) TIFF | 105247 (360) | Scheres
Beta-Gal | EMPIAR-10204 | EMD-6840 | 321.4GB | 2.6A (D2) | (3710,3838) 0.885 | 1338 (1-49) TIFF | ? | Kato
Relion3 | Tutorial |  | 3.1GB | 2.9A (D2) | (3710,3838) 0.885 | 24 (1-24) TIFF | ? (256) | Scheres
Denosing get 3.17A |  |  |  |  |  |  |  | 
tri-snRNP | EMPIAR-10073 | EMD-8012 | 75.2GB | 3.7A (C1) | ? 1.43 | ? | 473827 (3380) | Scheres
Dataset | Data | Model | Size | Res. | (Height, width) Pixel Size | Movie #(frame) | Particles | 
Beta-Gal | EMPIAR-10017 | EMD-2824 | 5.3GB | 4.2A (D2) | (4096,4096) 1.77 | 84(1) MRC | ? | Scheres
Relion2 | Tutorial |  | 4 GB | 7.3A (D2) | (1950,1950) 3.54 | 15(1-16) MRC |  | Scheres
Denosing get 7.3A |  |  |  |  |  |  |  | 
70S Ribosome | Test_Data | EMD-1056 | 0.7GB | 9A (C1) | ? 2.82 | ? |  | Scheres
80S Ribosome | EMPIAR-10028 | EMD-2660 | 1.2TB | 3.2A (C1) | (4096,4096) 1.34 | 1081 (1-16) TIFF |  | Scheres
Beta-Gal | EMPIAR-10204 | EMD-6840 | 321.4GB | 2.6A (D2) | (3710,3838) 0.885 | 1338 (1-49) TIFF | ? | Kato
Relion3 | Tutorial |  | 3.1GB | 2.9A (D2) | (3710,3838) 0.885 | 24 (1-24) TIFF |  | Scheres
Denosing get 3.17A |  |  |  |  |  |  |  | 
tri-snRNP | EMPIAR-10073 | EMD-8012 | 75.2GB | 3.7A (C1) | ? 1.43 | ? |  | Scheres

## Slide 14
Dataset | Method | Date | Size |  | Res. | Pixel Size |  | Movie |  | Particles | 
GS data | Krios+Falcon III |  | 60GB |  | ? | ? 0.85 |  | 558 MRC |  | 94154 (400400) | KpWu
Heterogenity observed using DRMRA |  |  |  |  |  |  |  |  |  |  | 
GS-Y398F-APO form |  | 2018.08.23 | 938 GB | ? (O) |  |  | (4096,4096) 0.85 |  | 603 (1-50) MRC | ? | KpWu
Apo-ferritin in RELION-3.0 | EMPIAR-10200 | EMD-0144 | 191.5 GB | 1.65A (O) |  |  | (3838,3710) 0.814 |  | 1255(1-40) TIFF | ? | Scheres
Apoferritin | Krios+Falcon III | 2018.08.30 | 643 GB | 2.7A (O) |  |  | (4096,4096) 0.85 |  | 411 (1-50) MRC | 86856 () | KpWu
Denoising from scratch get 6A |  |  |  | 3.48/3.04A (O) |  |  |  |  | 10 (1-50) | 4096 () | Apo_10
Apoferritin | Krios | 2018.11.08 | 469GB | 2.18 (O) |  |  | (4096,4096) 0.85 |  | 1022->300 (1-50) MRC | 368774 () | KpWu
 |  |  |  |  |  |  |  |  |  |  | Apo_11
Apoferritin | Krios | 2018.11.10 | 8TB | 1.96 (O) |  |  | ? 0.53 |  | 2600 (1-100) MRC |  | KpWu
Dataset | Method | Date | Size |  | Res. | Pixel Size |  | Movie |  | Particles | 
GS data | Krios+Falcon III |  | 60GB |  | ? | ? 0.85 |  | 558 MRC |  |  | KpWu
Heterogenity observed using DRMRA |  |  |  |  |  |  |  |  |  |  | 
GS-Y398F-APO form |  | 2018.08.23 | 938 GB | ? (O) |  |  | (4096,4096) 0.85 |  | 603 (1-50) MRC | ? | KpWu
Apo-ferritin in RELION-3.0 | EMPIAR-10200 | EMD-0144 | 191.5 GB | 1.65A (O) |  |  | (3838,3710) 0.814 |  | 1255(1-40) TIFF | ? | Scheres
Apoferritin | Krios+Falcon III | 2018.08.30 | 643 GB | 2.7A (O) |  |  | (4096,4096) 0.85 |  | 411 (1-50) MRC |  | KpWu
Denoising from scratch get 6A |  |  |  | 3.48/3.04A (O) |  |  |  |  | 10 (1-50) |  | Apo_10
Apoferritin | Krios | 2018.11.08 | 469GB | 2.18 (O) |  |  | (4096,4096) 0.85 |  | 1022->300 (1-50) MRC |  | KpWu
 |  |  |  |  |  |  |  |  |  |  | Apo_11
Apoferritin | Krios | 2018.11.10 | 8TB | 1.96 (O) |  |  | ? 0.53 |  | 2600 (1-100) MRC |  | KpWu

## Slide 15
Dataset | Data | Model | Size | Res. | Pixel Size | Movie | Particles | 
Brome Mosaic virus | EMPIAR-10010 | EMD-6000 | 1.7TB | 3.8A (I) | (4096,3072) 0.99 | 424 (1-37) TIFF | 35142 (420) | Wah Chiu
T20S | EMPIAR-10025 | EMD-6287 | 2.0TB | 2.8A (D7) | (7420,7676) 0.6575 | 196 (1-38) MRC | 49955 (448) | Carragher
CryoSparc | Tutorial |  | 8.1GB | 2.93A (D7) | (7420,7676) 0.6575 | 20 (1-38) TIFF | (4400) | CryoSparc
TRPV1 | EMPIAR-10059 | EMD-8117 | 93.8 GB | 2.95A (C4) | (3838,3710) 1.2156 | 1200(1) MRC | 218805 (192,192) | Gao and Cheng
Apo-Ferritin | EMPIAR-10248 |  | 145.9 GB | 1.54A (O) | (3710,3838) 0.495 | 972 (1-50) TIFF | ? | Kato
CisTEM | EMPIAR-10146 |  | 5.6GB | 3A (O) | (1240, 1200) 1.5 | 20 (1-50) MRC | ? | CisTEM
alcohol dehydrogenase | EMPIAR-10249 | EMD-0406 | 1.3T | 2.9A (C2) | (3710,3838) 0.5585 | 1153 (1-44) MRC | ? | Lander
Met-hemoglobin | EMPIAR-10250 | EMD-0407 | 1.9T | 2.8~3.2A (C2) | (3710, 3838) 0.5585 | 1665 (1-44) MRC | ? | Lander
PKA | EMPIAR-10252 | EMD-0409 | 5.5T | 6A (C1) | (3710, 3838) 0.5585 | 4812 (1-44) MRC | ? | Lander
Dataset | Data | Model | Size | Res. | Pixel Size | Movie | Particles | 
Brome Mosaic virus | EMPIAR-10010 | EMD-6000 | 1.7TB | 3.8A (I) | (4096,3072) 0.99 | 424 (1-37) TIFF |  | Wah Chiu
T20S | EMPIAR-10025 | EMD-6287 | 2.0TB | 2.8A (D7) | (7420,7676) 0.6575 | 196 (1-38) MRC |  | Carragher
CryoSparc | Tutorial |  | 8.1GB | 2.93A (D7) | (7420,7676) 0.6575 | 20 (1-38) TIFF |  | CryoSparc
TRPV1 | EMPIAR-10059 | EMD-8117 | 93.8 GB | 2.95A (C4) | (3838,3710) 1.2156 | 1200(1) MRC | 218805 (192,192) | Gao and Cheng
Apo-Ferritin | EMPIAR-10248 |  | 145.9 GB | 1.54A (O) | (3710,3838) 0.495 | 972 (1-50) TIFF | ? | Kato
CisTEM | EMPIAR-10146 |  | 5.6GB | 3A (O) | (1240, 1200) 1.5 | 20 (1-50) MRC | ? | CisTEM
alcohol dehydrogenase | EMPIAR-10249 | EMD-0406 | 1.3T | 2.9A (C2) | (3710,3838) 0.5585 | 1153 (1-44) MRC | ? | Lander
Met-hemoglobin | EMPIAR-10250 | EMD-0407 | 1.9T | 2.8~3.2A (C2) | (3710, 3838) 0.5585 | 1665 (1-44) MRC | ? | Lander
PKA | EMPIAR-10252 | EMD-0409 | 5.5T | 6A (C1) | (3710, 3838) 0.5585 | 4812 (1-44) MRC | ? | Lander

## Slide 16: ASCEP with Scipion2

## Slide 17: Enable Scipion2
gedit ~/.bashrc
  Add export PATH=/home/tlchen/scipion2/scipion:$PATH to the end the file
source ~/.bashrc
mv ~/.config/scipion/scipion.conf ~/.config/scipion/scipion1.conf
scipion config
  Press any key other than Enter
gedit ~/.config/scipion/scipion.conf
mkdir ~/ssd

## Slide 18: Back to Scipion1
gedit ~/.bashrc
  Comment out export PATH=/home/tlchen/scipion2/scipion:$PATH
source ~/.bashrc
mv ~/.config/scipion/scipion.conf ~/.config/scipion/scipion2.conf
mv ~/.config/scipion/scipion1.conf ~/.config/scipion/scipion.conf

## Slide 19: Import Project
直接在指令視窗打 scipion 即可開啟~~
需要重新開啟scipion才會看的到import的project

## Slide 20: Import/Export workflow
按下
Create Project
按下Create，就會出現操作介面

## Slide 21: Import/Export workflow
/home/tlchen/scipion_sinica/model_building.json

## Slide 22: Upload workflow
http://workflows.scipion.i2pc.es/

## Slide 23: Upload workflow

## Slide 24: Import/Export metadata/binaries

## Slide 25: Break
Now we should have 2 projects in scipion2
Image_proceesing (Full project)
Model_building (workflow)

## Slide 26: Basic Usage

## Slide 27
指令區
執行區
說明區
查看結果
Open image_processing project

## Slide 28
如果進到操作介面是凌亂的情況，或者需要對流程做整理，點選此圖，程式會自行整理順序。
可切換模式

## Slide 29
框框的顏色分為四種
1.藍色:代表只儲存操作指令，並未執行。
2.綠色:指令執行完。
3.黃色:指令執行中。
4.淡黃色:指令執行結束，還可以點進去繼續執行，
但底下有接其他指令不可再執行會出現錯誤。
5.紅色:出現錯誤。

## Slide 30
點選框框，按下滑鼠右鍵，會出現一排的選項，
:會出現指令操作
:複製此次的指令操作
:刪除此次操作，但有連接下一步，則無法刪除
:此次操作所存的檔案位置
:停止此操作，只有在運行中的指令才會出現
其他比較少使用就不介紹，但是可以去玩玩看。

## Slide 31
點選其中一個框框，在說明區會出現該指令的說明
1.Summary:
該指令輸入及輸入的資料訊息。
2.Method :方法說明及references。
3.Output Log: 程式執行過程。
以此圖為例，我們可以看到這個指令的
輸入資料是 outputMovies ，有15筆資料，影像大小1950950，有16張影像，pixel size為 3.54 A。
輸出資料是 outputmicographs，有15筆資料，影像大小1950950， pixel size為3.54 A。

## Slide 32
錯誤情況判斷查閱說明區 Output Log run stdout
若沒有出現紅字，有可能是執行到一半斷掉，重新執行即可。
若出現紅字，先改放入參數，再重新執行，或者選擇其他指令執行!!!
error
執行到一半斷掉

## Slide 33: Imports
點選
依照資料選擇輸入方式
1.資料檔案位置
2.資料名稱
*.mrc 代表讀取所有的 .mrc檔
填寫
Save 只會儲存輸入的訊息，並不會執行，
Execute 會儲存及執行此步驟。
3.按下Execute ，
執行此過程。
1
2
3

## Slide 34: 查看執行結果
由這裡可知共有15個movie，a每個movie有16張影像，
影像大小1950
1
2
點選這個綠色框框
點Aanlyze Results
點兩下會出現單張影像的圖像。
3

## Slide 35: Particle picking
1
2
按 找到要輸入的資料
3
4
圈選工具
圈particle 的標示
連續圈選，不好用
橡皮擦，用來刪除框框
調整框框size，可以先圈一個particle，再來回調整
下一頁
5
圈 particle
6
圈了一些particle 在按這個按鈕

## Slide 36
第6步這個動作會讓程式自己圈選，但是可以看到黃色框框區域還有些沒選到
7
按下 Reset Micrographs 使之全部重選
調整Threshod會影響最後particle選入的數量
8
9
在此只需做完一張 mircographs的 particle picking，其他張使用
Auto-picking

## Slide 37: Extract
1
2
3
按 找到要輸入的資料，
Particle box size 自行調整
Invert contrast : Yes !!
4
1. Invert contrast 改變 particle 的顏色，
慣用 白色 particle。
白色
黑色
2. Recommend
Xmipp extraction- for xmipp, eman2, sparx
Reion extraction- for cryosparc2 and relion (Especially in 3D part)
3. Bin the particle to speed up processing before 3D Refinement

## Slide 38: https://scipion-em.github.io/docs/docs/user/scipion-gui.html
隨意一張圖按下滑鼠右鍵會出現選項
Enable: 選入這個class
Disable:不要這個class
像這種只要丟棄第一個class，可以先對第一個class 點選disable，在點
SelectALL。
2
1
ShowJ

## Slide 39
1
點選這個綠色框框
點Aanlyze Results
2
可以看到particle 的分層，如果想看3D圖，
點選chimera
ShowJ

## Slide 40
當你點下Aanlyze Results，並沒有出現分組結果，而是出現下列這些框框，此時請點 ，
就會出現執行結果。
relion
cl2d
Other viewer/statistics

## Slide 41: MPI/GPU
1
2
按 找到要輸入的資料
3
使用CPU個數，可自行調整，

## Slide 42: MPI/GPU
浮標指向其中一個框框，停留一段時間，會出現該指令執行時間。

## Slide 43: Consensus protocols
Picking
CTF – estimations must agree below certain resolution
Classes – intersection of assignment
Angular

## Slide 44: Pruning and Validation
Re-projection consistency
Angular distribution
Histogram of statistics
2D plots

## Slide 45: Break
Manual
https://github.com/I2PC/scipion/wiki/tutorials/scipion_tutorial_betagal.pdf
Or 卉倫的ppt
CryoSparc2的帳號密碼
  steve2003121.eecs96@g2.nctu.edu.tw
  stats328

## Slide 46: Advance

## Slide 47: 尋找輸出資料路徑
點選需要的輸出資料的框框，按下滑鼠右鍵，會出現一排的選項，點取 Brower
大多數的資料都存在extra 裡面
1
2
3
有了路徑就能從外部的資料夾找到檔案，
也可以透過 ftp直接到從資料夾載資料。

## Slide 48: 下載需要的參數資訊
點選需要的輸出資料的框框，按下滑鼠右鍵，會出現一排的選項，點取 Brower
1
2
3
點選有 這個符號的檔案
下一頁
4
點選Browse Data
假設今天我想下載 movement alignment 的位移資訊

## Slide 49
找到我們要的資料位置，
在此為c13、c14
5
6
將Table的地方調成Objects
複製c13、c14行的資料到這裡
7
8
10
調整檔案位置及名稱，名稱記得打上 .txt
9

## Slide 50: Recommend method
Stage | CPU | GPU
Motion Correction | Unblur | MotionCor2
CTF Estimation | Ctffind4 | Gctf
Particle Picking | Xmipp Relion | CrYolo Topaz
Particle Extraction | Xmipp Relion | 
2D Classification | ISAC CL2D | Relion CryoSparc GL2D
3D Initial Model | Simple Eman2 | CryoSparc
3D Classification/ Validation | Xmipp Validation tool | Relion 3D Classification/Multibody Refinement CryoSparc Nonuniform/Local Refinement
3D Refinement | Xmipp High Res | Relion CryoSparc
Polishing |  | Relion CTF Refinement Relion Bayesian Polishing

## Slide 51: Model Building

## Slide 52: Resolution revolution

## Slide 53: Resolution revolution
https://www.sciencedirect.com/science/article/pii/S1369527417300607?via%3Dihub

## Slide 54
Atomic model
(Khoshouei et al., 2017)
Approach to the problem
Electron density map
SPA workflow
2 Hemoglobin subunit a (141 aa)
2 Hemoglobin subunit b (146 aa)
4 HEME
www.cellsignal.com
Model building

## Slide 55: Template-Free (De-novo)
將鍵長、鍵角、二面角、凡得瓦作用力、靜電力及 氫鍵等相關能量考慮進來。
利用分子力學力場方法，輕微地改變分子的幾何結構，便能最佳化一個分子 單一構型的結構，並產生較合理的結構。
從sequence 預測三維結構

## Slide 56: Template-Free (De-novo) using machine learning
Deep learning Method
  AlphaFold (MiniFold)
  Recurrent Geometric Networks
  Predict Contact Map
  Predict Structure
Database
  Critical Assessment of protein
  Structure Prediction (CASP)
  ProteinNet
Notes: https://en.wikipedia.org/wiki/Protein_contact_map

## Slide 57: Template-Based (Comparative modeling)
Select reference protein that is similar to target protein
  The tertiary structure of reference protein is known
  The sequence similarity between target and reference is higher than 25%
Multiple sequence alignment
Identify backbone and variation part
Variation part are determined by
  Search database the corresponding structure fragment
  Adjust the coordinates by minimizing the energy
Refinement and validation
Notes: 該蛋白質已知的實驗數據做一致性的比較來評估，例如溶劑分子的可接觸性，胺基酸堆積密度、厭水性或帶電荷或極性胺基酸的位置，分子靜電位場分佈和溶解自由能等等實驗測量值
http://biobug.life.nthu.edu.tw/mod/homology/teachchinese.htm?fbclid=IwAR0XJQ7jdvKxaOflsuWFDv-PAPL9YInInVs8riemKnlXE57wbROIxoJTRoQ

## Slide 58
Our inputs will be map and protein sequences
Overview

## Slide 59
Model building
Basic steps
Tools

## Slide 60
1.- Get the initial model (s)
Homology modeling
Our proteins borrow
the structure
of similar proteins
1st clue:
Skeleton of a carbons
and
many side chains
2 Hemoglobin subunit a (141 aa)
2 Hemoglobin subunit b (146 aa)
4 HEME
www.cellsignal.com

## Slide 61
2.- Rigid fitting of model(s) in map

## Slide 62
2.- Rigid fitting of model(s) in map

## Slide 63
2.- Rigid fitting of model(s) in map

## Slide 64
2.- Rigid fitting of model(s) in map

## Slide 65
2.- Rigid fitting of model(s) in map

## Slide 66
3.- Flexible fitting (refinement) of model(s) in map
Get the final model(s)
Manual and automatic
Minimize E = Egeom + w Edata in Real space or Fourier space

## Slide 67
Geometry
Map and model
similarity
Is this structure reliable?
4.- Model(s) validation
Is the map derived from
the model similar to the
original map?
Q (Submission)
Is this structure similar
to structures of the database?
(Bond lengths, angles, contacts …)
PDB

## Slide 68
Model building
Basic steps
Tools
1.- Get the initial model (s)
2.- Rigid fitting of model(s) in map
3.- Flexible fitting (refinement)
of model(s) in map
4.- Model(s) validation
the problem
0.- Map preprocessing

## Slide 69
0.- Map preprocessing
Map sharpening
Extract unit cell
Ramírez-Aportela et al., 2018
sym C8

## Slide 70
Model building
Basic steps
Tools
1.- Get the initial model (s)
2.- Rigid fitting of model(s) in map
3.- Flexible fitting (refinement)
of model(s) in map
4.- Model(s) validation
the problem
0.- Map preprocessing

## Slide 71
Model building
Basic steps
Tools
1.- Get the initial model (s)
2.- Rigid fitting of model(s) in map
3.- Flexible fitting (refinement)
of model(s) in map
4.- Model(s) validation
the problem
0.- Map preprocessing

## Slide 72
* Borrowed from crystallography
* Specifically designed for cryo-EM data
Tools
(Cassidy et al.)

## Slide 76
https://github.com/I2PC/scipion/wiki/tutorials/tutorial_model_building_basic.pdf

## Slide 77
subunit a (141 aa)
subunit a (141 aa)
subunit b (146 aa)
subunit b (146 aa)
sym C2; 3.2 Å resolution
Human Haemoglobin
(Khoshouei et al., 2017)

## Slide 78
subunit a (141 aa)
subunit a (141 aa)
subunit b (146 aa)
subunit b (146 aa)
sym C2; 3.2 Å resolution
Human Haemoglobin
(Khoshouei et al., 2017)

## Slide 79
MODELING WORKFLOW IN SCIPION
Other seqs
Hgb sharpened map
Sym C2
Preprocessing
Import
Local deblur
Local resolution
Create 3D mask
Hgb map
aHgb seq
Extract unit cell
Chimera rigid fit
Powerfit
Rigid fitting
1pbx
Search for
homologous sequences
PDB
Import
aHgb seq
a1pbx seq
Other seqs
Initial
model
http://bangqu.com/699cr9.html

## Slide 80
Validation
Validation
MODELING WORKFLOW IN SCIPION
Flexible fitting
Chimera rigid fit
Powerfit
Rigid fitting
CCP4 Coot
phenix - molprobity
phenix - emringer
phenix - molprobity
phenix - emringer
phenix - molprobity
phenix - emringer
Phenix – real space refine
CCP4 refmac
Export to EMDB
Export to EMDB
Export to EMDB

## Slide 81: Break
Manual
  https://github.com/I2PC/scipion-courses/wiki/july_8_2019
  https://github.com/I2PC/scipion/wiki/tutorials/tutorial_model_building_basic.pdf
  搜尋map對應的target sequence https://www.rcsb.org/
  搜尋同源sequence and structure https://blast.ncbi.nlm.nih.gov/Blast.cgi?PAGE=Proteins
  Modeller license key
    MODELIRANJE